## Slide 1: BGP in 2013
Geoff Huston
APNIC
IEPG @ IETF89

## Slide 2
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
Quoted from a 2012 research paper on routing

## Slide 3
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
quote from a 2012 research paper on routing
Is this really true, or do we accept it as true without actually looking at the real behaviours of the Internet’s routing system???

## Slide 4
In this presentation we’ll explore the space of inter-domain routing and look at
  the growth of the eBGP routing table over time and some projections for future growth
  the extent to which more specifics are dominating routing table growth ... or not

## Slide 5: The Big Picture of the v4 Routing Table

## Slide 6: The Big Picture of the v4 Routing Table
Introduction of
CIDR – March 1994
The Great Internet Boom
and Bust of 2000/2001
Broadband to the Masses
The GFC hits the Internet
Address Exhaustion

## Slide 7: The Routing Table in 2012-2013
Lets look at the recent past in a little more detail...

## Slide 8: IPv4 BGP Prefix Count 2011 - 2013
Jan
2011
Jan
2012
340,000
440,000
540,000
Jan
2013
Jan
2014

## Slide 9: IPv4 BGP Prefix Count 2013
Jan
2013
Apr
2013
430,000
460,000
490,000
Jul
2013
Oct
2013
25th June added HE to the upstream transit set
side effect of adding 10K
more specifics
AS 7029 +3,606
AS 33363 +1,651
AS 4323 +1,351
AS 9116 + 348
Jan
2014

## Slide 10: IPv4 BGP Prefix Count 2013
Jan
2013
Apr
2013
430,000
460,000
490,000
Jul
2013
Oct
2013
Jan
2014

## Slide 11: IPv4 Routed Address Span: 2011 - 2013
130/8s
140/8s
150/8s
Jan
2011
Jan
2012
Jan
2013
Jan
2014

## Slide 12: IPv4 Address Pool

## Slide 13: IPv4 Address Pool

## Slide 14: That Unadvertised Address Pool
Appears to be relatively static in size since early 2011 at some 50 /8s, or 20% of the IPv4 global unicast space
At this stage its likely that ARIN and LACNIC will both hit their address pool exhaustion threshold levels at the end of 2014

## Slide 15: IPv4 Routed AS Count
40,000
44,000
2010
2011
Jan
2011
Jan
2013
Jan
2012
Jan
2014
Jan
2015
36,000
48,000

## Slide 16: IPv4 2011 BGP Vital Statistics
Jan-13 Jan-14
Prefix Count 440,000 488,000 +11%
Roots 216,000 237,000 +10%
More Specifics 224,000 251,000 +12%
Address Span 156/8s 159/8s + 2%
AS Count 43,000 46,000 + 7%
Transit 6,100 6,600 + 8%
Stub 36,900 39,400 + 7%

## Slide 17: IPv4 in 2013 – Growth is Slowing
Overall Internet growth in terms of BGP is at a rate of some ~8-10% p.a.
  This is down by 33% from 2010
There was a single announcement event on 25 June of some 10K additional routes
Address span growing far more slowly than the table size

## Slide 18: IPv6 BGP Prefix Count
2,000
12,000
20,000
Jan
2011
Jan
2012
Jan
2013
Jan
2014
4,000

## Slide 19: IPv6 BGP Prefix Count
2,000
12,000
20,000
Jan
2011
Jan
2012
Jan
2013
Jan
2014
4,000
World IPv6 Day

## Slide 20: IPv6 Routed Address Span
Jan
2013
Jan
2012
Jan
2014
Jan
2015
0
30,000
60,000
90,000
Jan
2011

## Slide 21: IPv6 Routed AS Count
Jan
2011
Jan
2013
Jan
2012
Jan
2014
2,000
6,000
8,000
10,000
4,000
Jan
2015
World IPv6 Day

## Slide 22: IPv6 2011 BGP Vital Statistics
Jan-13 Jan-14 p.a. rate
Prefix Count 11,500 16,100 + 40%
Roots 8,451 11,301 + 34%
More Specifics 3,049 4,799 + 57%
Address Span (/32s) 65,127 72,245 + 11%
AS Count 6,560 7,845 + 20%
Transit 1,260 1,515 + 20%
Stub 5,300 6,330 + 19%

## Slide 23: IPv6 in 2013
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2011 growth rate was ~ 90%.
(Looking at the AS count, if these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in16 years time -- 2030!)

## Slide 24: BGP Size Projections
Generate a projection of the IPv4 routing table using a quadratic (O(2) polynomial) over the historic data
  For IPv4 this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
  which makes this projection even more
  speculative than normal!

## Slide 25: IPv4 Table Size
2004
2010
0
600,000
2006
2012
2014
200,000
400,000
Linear: Y = -1692020 + (t * 1572.086)
Quadratic: Y = -2531405 + (2.824.189 * t) + (-4.667387* 10-13 * t2)
Exponential: Y = 10**(3.403664 + (year * 1.650395e-09))
2008
2016

## Slide 26: Daily Growth Rates
2006
2010
-800
0
800
2008
2012
2014
-400
400

## Slide 27: IPv4 BGP Table Size predictions
Jan 2013 441,172 entries
2014 488,011 entries
2015 540,000 entries 559,000
2016 590,000 entries 630,000
2017 640,000 entries 710,000
2018 690,000 entries 801,000
2019 740,000 entries 902,000
* These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.
Linear Model
Exponential Model

## Slide 28: IPv6 Table Size
2006
2010
0
20,000
30,000
2008
2012
2014
10,000
2016
40,000

## Slide 29: Daily Growth Rates
2006
2010
-40
0
40
2008
2012
2014
-20
20

## Slide 30: IPv6 BGP Table Size predictions
Jan 2013 11,600 entries
2014 16,200 entries
2015 25,400 entries 19,000
2016 38,000 entries 23,000
2017 57,000 entries 27,000
2018 85,000 entries 30,000
2019 127,000 entries 35,000
* These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.
Exponential Model
LinearModel

## Slide 31: Up and to the Right
Most Internet curves are “up and to the right”
But what makes this curve painful?
  The pain threshold is approximated by Moore’s Law

## Slide 33
Moore’s Law
BGP Table Size Predictions
IPv4 BGP Table size and Moore’s Law

## Slide 34: IPv6 Projections and Moore’s Law
Moore’s Law
BGP Table Size Predictions

## Slide 35: eBGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing rapidly, is still relatively small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm it will continue to be viable for some time yet

## Slide 36: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 37: Announcements and Withdrawals

## Slide 38: Unstable Prefixes

## Slide 39: Convergence Performance

## Slide 40: IPv4 Average AS Path Length
Data from Route Views

## Slide 41: Updates in IPv4 BGP
Nothing in these figures is cause for any great level of concern …
  The number of unstable prefixes per day is growing at a slightly lower rate than the number of announced prefixes
  The number of updates per instability event has been constant, due to the damping effect of the MRAI interval, and the relatively constant AS Path length over this interval
What about IPv6?

## Slide 42: Announcements and Withdrawals

## Slide 43: Unstable Prefixes

## Slide 44: Convergence Performance

## Slide 45: IPv6 Average AS Path Length
Data from Route Views

## Slide 46: BGP Convergence
The long term average convergence time for the IPv4 BGP network is some 70 seconds, or 2.3 updates given a 30 second MRAI timer
The long term average convergence time for the IPv6 BGP network is some 90 seconds, or 3 updates

## Slide 47: BGP Table Growth
However ... continued scalability of the routing system relies on continued conservatism in routing practices.
How good are we at “being conservative” in routing?

## Slide 48: CIDR and BGP
To what extent do we still practice “conservative” routing and refrain from announcing more specifics into the routing table?
Are we getting better or worse at aggregation in routing?
What is the distribution of advertising more specifics? Are we seeing a significant increase in the number of more specific /24s in the routing table?

## Slide 49: An Example:
Prefix AS Path
193.124.0.0/15 4608 1221 4637 3356 20485 2118 ?
193.124.0.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.1.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.2.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.3.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.4.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.5.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.6.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.7.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.8.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.9.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.10.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.11.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.12.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.13.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.14.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.15.0/24 4608 1221 4637 3356 20485 2118 ?
Origin AS: AS 2118 RELCOM-AS OOO "NPO Relcom"

## Slide 50: Who is doing this the most?
www.cidr-report.org

## Slide 51: More specifics in the Routing Table
Total Table Size
More Specifics

## Slide 52: More specifics in the Routing Table
Since 2002 more specifics account for ~50% of the
Routing Table. This has been a relatively constant
proportion over the past 12 years

## Slide 53: How much address space is announced by more specifics?
% of address space announced by more specifics –
-- as seen by peers of Route Views

## Slide 54: Does everyone announce more specifics?
332 Origin AS’s announce 50% of the total set of more specifics!

## Slide 55: Is it Everyone?
1% of the ASes (458 ASes) announce 54% of the more specifics (133,688 announcements)
55% of the ASes announce no more specifics
The top 20 ASes announce 40,404 more specifics

## Slide 56: More specifics in the V6 Routing Table
Total Table Size
More Specifics

## Slide 57: More specifics in the V6 Routing Table

## Slide 58: How much V6 address space is announced by more specifics?
% of address space announced by more specifics –
-- as seen by peers of Route Views

## Slide 59: Are We Getting Any Better?
Take the daily top 10 ASes of advertisers of more specifics over the past 3 years and track the number of more specifics advertised by these ASes over the entire period

## Slide 60: Are We Getting any Better?
These AS’s were seen to be advertising the highest number of more specifics over the past 3 years:
1785 AS-PAETEC-NET - PaeTec Communications, Inc. US
2118 RELCOM-AS OOO "NPO Relcom" RU
3352 TELEFONICA-DATA-ESPANA TELEFONICA DE ESPANA ES
3356 LEVEL3 Level 3 Communications US
4323 TWTC - tw telecom holdings, inc. US
4538 ERX-CERNET-BKB China Education and Research Network Center CN
4755 TATACOMM-AS TATA Communications formerly VSNL is Leading ISP IN
4766 KIXS-AS-KR Korea Telecom KR
6389 BELLSOUTH-NET-BLK - BellSouth.net Inc. US
6503 Axtel, S.A.B. de C.V. MX
7011 FRONTIER-AND-CITIZENS - Frontier Communications of America, Inc. US
7029 WINDSTREAM - Windstream Communications Inc US
7545 TPG-INTERNET-AP TPG Telecom Limited AU
8402 CORBINA-AS OJSC "Vimpelcom" RU
10620 Telmex Colombia S.A. CO
11492 CABLEONE - CABLE ONE, INC. US
15557 LDCOMNET Societe Francaise du Radiotelephone S.A FR
17974 TELKOMNET-AS2-AP PT Telekomunikasi Indonesia ID
18566 MEGAPATH5-US - MegaPath Corporation US
22773 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications Inc. US
28573 NET Servicos de Comunicatio S.A. BR
33363 BHN-TAMPA - BRIGHT HOUSE NETWORKS, LLC US
36998 SDN-MOBITEL SD

## Slide 61: Yes ... and No

## Slide 62: Are We Getting Any Better?
Some ASes are effectively reducing the number of more specifics that are advertised into the global routing system
Some ASes are increasing the number of more specifics
And some are consistently advertising a significant number of more specifics
There is no net change in the overall distribution and characteristics of more specifics in the routing system.

## Slide 63: Why advertise a more specific?
The reasons why we see more specifics in the routing system include:
  Different origination (“hole punching” in an aggregate)
  Traffic engineering of incoming traffic flows across multiple inter-AS paths
  “protection” against route hijacking by advertising more specifics
  Poor routing practices

## Slide 64: Types of More Specifics
Hole Punching
Traffic Engineering
Senseless Routing Vandalism

## Slide 65: Types of More Specifics
Hole Punching?
Traffic Engineering?
Senseless Routing Vandalism?

## Slide 66: Daily Update Rates
Do more specifics experience a higher update rate than aggregate advertisements?
Lets examine the past 3 years of updates and examine the daily count of prefix updates for root aggregates and more specifics

## Slide 67: Daily BGP Updates

## Slide 68: Relatively Speaking

## Slide 69: More Specifics

## Slide 70: Daily Update Rates
Do more specifics generate a higher update rate than aggregate advertisements?
    Yes – in terms of prefix updates, more specifics are some 4 times noisier than the aggregates in terms of update traffic totals
    More Specifics that “hole punch” (different origin AS) tend to be relatively noisier than other forms of more specifics
Is this because they are less stable or noisier?

## Slide 71: Stability of More Specifics
Less Stable
More Stable
Hole Punching?
Traffic Engineering?
Senseless Routing Vandalism?

## Slide 72: What are we seeing?
The profile of updates in BGP is dominated by the instability of the more specific announcements, which are 4 x more likely to experience instability compared to aggregate advertisements
With the set of more specifics, “hole punching” (different origin AS, different AS Path) is consistently less stable than the other two types of more specifics.

## Slide 73: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention

## Slide 74: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
Could we do better?
  Yes!
  Filtering out more specifics will both reduce table size and also reduce the level of dynamic update in the inter-domain environment

## Slide 75: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
Should we do better?
  It can be difficult to justify the effort and the cost: the current growth rates of the routing table lie within relatively modest parameters of growth and still sit within the broad parameters of constant unit cost of routing technology
  On the other hand, we need to recognize that we could do a lot better in terms of eliminating routing noise, and achieve this with with a relatively modest amount of effort

## Slide 76
Thank You
Questions?